## Slide 1: Artificial Intelligence-Based Handoff Management for Dense WLANs: A Deep Reinforcement Learning Approach ZIJUN HAN, TAO LEI, ZHAOMING LU, XIANGMING WEN, WEI ZHENG, (Member IEEE), AND LINGCHAO GUO IEEE ACCESS
Notes: 다.

## Slide 2: Contents
Background
Problem
Architecture
System Model
Proposed Scheme
Algorithm
Experiment
Conclusion
Notes: 발표 순서는 다음과 같습니다

## Slide 3: Background
There are no mechanisms for ensuring the seamless handoff. Typically the handoff delay in WLAN is approximately 300 ms or more
SDN controller can give a global view of the network so that real-time network status and statistics can be detected through OpenFlow protocol
For SDN-based WLAN, there is no channel scanning in discovery process
The network is dynamic. So self learning is required
Notes: 오늘 세미나 할 내용을 간단히 설명드리자면

## Slide 4: Problem
Focusing on improving the data rate during handoff process by selecting AP
RL can be solution for self-learning
  There is Q-learning
  However, Q-learning cannot achieve desired results in the case of the infinite numbers of state space
  So, DQN is used

## Slide 5: Architecture
DQN Architecture
  Each network used to extract feature
    CNN: spatial location of STA
    RNN: temporary feature like mobile velocity
  Deep Neural Network is leveraged to realize the mapping of state to action
Notes: 앞에서 정의한 State, Action, Reward를 가지고 DQN 동작
State에서 CNN을 거치고 RNN을 거치고 Decision module을 거치면서 Action을 생성한다.
생성된 Action을 통해 Reward를 계산하고 그 Reward를 바탕으로 네트워크를 수정

## Slide 6: RNN(Recurrent Neural Network)
A recurrent neural network (RNN) is a class of artificial neural networks where connections between nodes form a directed graph along a temporal sequence
This allows it to exhibit temporal dynamic behavior.
Unlike feedforward neural networks, RNNs can use their internal state (memory) to process sequences of inputs
< https://dreamgonfly.github.io/rnn/2017/09/04/understanding-rnn.html >
Notes: 시퀀스가 시간에 따른 SINR
Hidden state
  기존의 Neural Network와 달리 Hidden state 개념(기억과 유사)을 가짐
  Hidden state는 지금까지 입력된 데이터를 요약한 정보
  새로운 데이터가 들어올 때마다 Hidden state(기억)를 수정
  모든 입력을 다 처리하고 난 후 network에 남겨진 Hidden state는 시퀀스 전체를 요약한 정보

## Slide 7: System Model
SDN-based WLAN
  M APs and N STAs
  Focus on the handoff scheme under the condition of uplink traffic
Log-distance Path Loss Model
  This model is leveraged to serve as the channel transmission model
  The uplink RSS detected on at the distance from can be assigned by
    Where represents the transmitting power of STAs, and are the transmitting and receiving antenna gain respectively. f denotes the frequency band, is the reference distance to calculate the loss. L is the system loss, c corresponds to the light velocity and represents the path loss factor

## Slide 8: System Model
SINR
  The uplink SINR from to is
    Where indicates the cumulative interference caused by other STAs. and is additive white Gaussian noise

## Slide 9: Proposed Scheme
State
  At time n, the state perceived by the agent module is defined as
    Where is the state information (i.e., SINR) perceived on and is the number of APs
  The agent module termly refreshes the state at a time interval , and preprocesses state to an image-like tensor,
    Where is the time length for perceiving, indicating the size of the reformulated tensor for feature extraction. It depends on the actual networks

## Slide 10: Proposed Scheme
Action
  The control action is denoted by and takes on one of the values 1,2,…,M, determining the handoff to target AP. That is
Reward
  Take the real-time uplink throughput as the reward r

## Slide 11: Algorithm

## Slide 12: Experiment
Environment
  The WLAN system model is established by means of Mininet-WiFi emulator
  The learning phase is implemented on TensorFlow, a Google’s open source platform for deep learning
  Analysis considers a dense WLAN consisting of 9 APs and 12 STAs
  Among the STAs, one serves as a mobile object observed by the agent module, while others are stationary to produce background traffic
  The observed STA moves randomly throughout the radio coverage areas

## Slide 13: Experiment
Other tools
  Iperf
    A survey instrument for network performance, is leveraged to measure the throughput between two ports by creating data stream
  tcpdump
    Its command is adopted to capture time stamp of packets to depict the variations in throughput
  iw
    In response to the handoff instructions made by the decision module

## Slide 14: Experiment
Scheme
  Takes the following three representative handoff schemes as the control group, and carries out two experiments and to demonstrate the effectiveness of DCRQN
  RSST based handoff scheme
    It is traditional WLAN handoff scheme
    Handoff
      When the RSS drops to (-58dBm);
      When the difference value of uplink RSSs between the largest one from neighboring Aps and serving AP exceeds (5dBm), the largest one serves as the target AP
  RSSS based handoff scheme
    It is the SDN-based RSST scheme
    The STA needs no channel scanning when performing handoff
  DQNH based handoff scheme
    Similar to DCRQN, However, it involves no feature extraction module

## Slide 15: Experiment
Parameters

## Slide 16: Experiment
Neural Network
  CNN
    16 kernels that each size is 5 x 5, activation function is ReLU
    32 kernels that each size is 3 x 3, activation function is ReLU
    Max pooling function, kernel is 2 x 2
  RNN
    Two RNN cells that each size is 256, activation function is tanh
  DNN
    Two fully connected layers, sizes are 256, 128, activation function is ReLU

## Slide 17: Experiment
Experiment
  Compare the trend of throughput variation in the case of a single handoff

## Slide 18: Experiment
Experiment

## Slide 19: Experiment
Experiment

## Slide 20: Conclusion
Focus on the handoff management scheme in the SDN based WLAN
Propose DCRQN, a novel DQN-based handoff decision algorithm where SINR is leveraged to characterize the STA’s state
Besides, CNN and RNN are resorted to extract the fine-grained features of the wireless signals, respectively
The experimental results show that the proposed scheme can significantly improve the data rate during the handoff process, outperforming the traditional handoff scheme

## Slide 21: Research
Consider network and state
  In this paper, there is preprocessing process
  State will be consist of timeslot (resource)
  will check that state is configured correctly for neural network