## Slide 1: How Much Can Visual Quality of HTTP Adaptive Streaming Be Improved By Cooperative SDN-enabled Wi-Fi APs? Jae Jun Ha Media Computing and Networking Laboratory POSTCH 2020-06-23
Notes: 제목에 관한 문의

## Slide 2: Contents
Introduction
Proposed Video Streaming Service
  System Architecture
  Problem Description
  Proposed Algorithm
Experimental Results
  Experimental Environments
  Performance Comparison with Other Algorithms
Conclusion
Notes: 30초

## Slide 3
Introduction

## Slide 4: Introduction
Trend of traffic
  The total number of Internet users is expected to increase from 3.9 billion in 2018 to 5.3 billion in 2023.
  Video streaming had heavy effect on traffic
  Over time, clients want higher quality video streaming.
Cisco, “Cisco Annual Internet Report, 2018-2023 White Paper,” Cisco, San Jose, CA, USA, Mar. 2020.
Notes: 30초
인터넷 사용자 증가  traffic 증가  bandwidth 관리 필요
특히 고품질의 비디오 스트링 서비스 요청 증가 (더 많은 대역폭이 필요)

## Slide 5: Introduction
DASH (Dynamic Adaptive Streaming over HTTP)
  It is one of the adaptive bitrate streaming technologies that enables high quality streaming of media over the Internet, delivered from a traditional HTTP web server.
1 Mbps
500 Kbps
10 Mbps
1 Mbps
10 Mbps
500 Kbps
Video
Video Segments
Several encoding bitrate
DASH Server
DASH Client
DASH Client
DASH Client
Notes: 1분
이러한 video traffic을 다루기 위한 기술로써 DASH가 있습니다.
세그먼트 잘게 쪼개 저장하는 것 설명

## Slide 6: Introduction
Problem of DASH
  However, DASH streaming has big issue.
  Because this streaming technology considers each client situation, not the overall client, it causes unfairness of the overall resource usage.
    480p
    480p
    1080p
    144p
< Ideal case >
< A specific client preempts resource >
Notes: 1분
전체가 아닌 각 클라이언트 상황만 고려  자원 사용의 불공정성

## Slide 7: Introduction
SDN (Software Defined Networking)
  SDN is composed of a structure that separates data planes and control planes of network equipment. It connects controllers and network equipment using Open Flow API.
  Through the centralized structure on the controller, overall network is controlled. It enables efficient use of the network.
Controller
OpenFlow Control
Network Fabric
Network
Applications
Network
Applications
SDN
Clients
API
Notes: 1분

## Slide 8: Introduction
Limitation
  SDN enabled DASH can only be used in enterprise / private networks
  Bitrate adjustment is against network neutrality
    This system intervenes end-to-end
  It can be used with permission
Notes: 30초
해당 시스템에서는 SDN을 이용해서 bitrate를 전체적인 관점에서 제어하려고 한다.
그런데 SDN을 사용시 주의할 점이 있다.

## Slide 9: Introduction
Multiple Wi-Fi connection
  The wireless network situation is changing rapidly. So, it is necessary to use the resource according to the situation.
  Through multiple interfaces, chunks can be received differently depending on the unstable wireless network situation.
Network B
Network A
Notes: 30초

## Slide 10
Proposed Video Streaming Service
System Architecture

## Slide 11: System Architecture
  The system consists of four elements.
MPD
HTTP Server
Segments
MPD
SDN Controller
Multipath Agent
SDN Application
OVS
Media Server
Segments
AP Agent
Traffic Info Transmitter
Hostapd
Open Flow
Traffic Info Transmitter
DASH Client
Traffic Info Collector
Streaming Optimizer
HTTP Server
Notes: 3분

## Slide 12: System Architecture
  SDN Application periodically collects resource information.
  Based on the collected resources, the bitrate and delivery ratio of the client are determined.
MPD
HTTP Server
Segments
MPD
SDN Controller
Multipath Agent
SDN Application
OVS
Media Server
Segments
AP Agent
Traffic Info Transmitter
Hostapd
Open Flow
Traffic Info Transmitter
DASH Client
Traffic Info Collector
Streaming Optimizer
HTTP Server
Notes: 3분

## Slide 13: System Architecture
  Media Server keeps MPD (Media Presentation Description) and videos.
  it keeps the videos in segment units according to the encoding rate.
MPD
HTTP Server
Segments
MPD
SDN Controller
Multipath Agent
SDN Application
OVS
Media Server
Segments
AP Agent
Traffic Info Transmitter
Hostapd
Open Flow
Traffic Info Transmitter
DASH Client
Traffic Info Collector
Streaming Optimizer
HTTP Server
Notes: 3분

## Slide 14: System Architecture
  AP agent periodically provides resource information to SDN application.
MPD
HTTP Server
Segments
MPD
SDN Controller
Multipath Agent
SDN Application
OVS
Media Server
Segments
AP Agent
Traffic Info Transmitter
Hostapd
Open Flow
Traffic Info Transmitter
DASH Client
Traffic Info Collector
Streaming Optimizer
HTTP Server
Notes: 3분

## Slide 15: System Architecture
  DASH Client is a client that receives video streaming.
  DASH Client connects to multiple APs using multiple interfaces.
  Bitrate and delivery ratio are controlled by SDN Application.
MPD
HTTP Server
Segments
MPD
SDN Controller
Multipath Agent
SDN Application
OVS
Media Server
Segments
AP Agent
Traffic Info Transmitter
Hostapd
Open Flow
Traffic Info Transmitter
DASH Client
Traffic Info Collector
Streaming Optimizer
HTTP Server
Notes: 3분

## Slide 16
Proposed Video Streaming Service
Problem Description

## Slide 17: Problem Description
Problem Formulation
Determine | so as to
Maximize | 
subject to | 
 | and
Determine | 
Maximize | 
subject to | 
Symbol | Description
 | The delivery ratio that receives through
 | Bitrate that receives streaming service
 | Bitrate that wants to receive streaming service
 | The number of UE s
 | The number of AP s
 | PSNR parameter (depended on video)
 | Bandwidth between and
 | DASH segment length
 | Manage resource in terms of time
 | Median value of s’ buffer
 | Buffer threshold
 | Buffer control function
 | Buffer parameter
Symbol | Description
 | The number of UE s
 | The number of AP s
 | PSNR parameter (depended on video)
 | DASH segment length
 | Manage resource in terms of time
 | Buffer threshold
 | Buffer control function
( )
Notes: 품질은 PSNR을 사용했으며 이는 로그함수로 정의하였다. 로그 함수가 비디오 RD 커브의 속성을 잘 다룰 수 있으며 또한 Proportional fairness를 잘 고려할 수 있기 때문이다.
시간의 관점으로 자원을 관리하는 이유는 DASH Client의 버퍼 상태를 고려하기 위함이다.
S(t)는 Underflow 발생을 막기 위해 Buffer occupancy 조절하기 위한 함수
버퍼 Threshold를 기준으로 사용자 버퍼에 쌓인 데이터 양이 적으면 버퍼 underflow를 방지하기 위해 타임 슬롯을 줄여 사용자들의 비트레이트를 낮춘다.
반대로 사용자 버퍼에 쌓인 데이터 양이 많으면 영상의 품질을 높이기 위하여 bitrate를 높인다.
해당 연구에서는 bitrate를 Lagrange Multiplier로 사용해서 구한다.

## Slide 18: Problem Description
Lagrange Function
  Too many lambdas
VAP (Virtual Access Point)
  Like one AP (one lambda)
Notes: 2분
Lagrange Multiplier는 최적화의 한 방법입니다.
Optimal solution 풀기 위해 Lagrange Multiplier 사용 한다는 것 설명
Lagrange Multiplier를 사용할 경우 AP 하나당 람다가 생긴다
여러 람다가 생길 경우 람다 간에 dependency가 생겨 복잡 해져서 람다 값들을 구할 수 없다.
그래서 값을 정한다.
2분
Optimal solution 풀기 위해 Lagrange Multiplier 사용 한다는 것 설명
Lagrange Multiplier를 사용할 경우 AP 하나당 람다가 생긴다
여러 람다가 생길 경우 람다 간에 dependency가 생겨 복잡 해져서 람다 값들을 구할 수 없다.
그래서 𝑥_(𝑖,𝑗) 값을 정한다.

## Slide 19
Proposed Video Streaming Service
Proposed Algorithm

## Slide 20: Algorithm
Over AP’s timeslot
Request with
Provide streaming with
no
Initialize and
and
or
and
Calculate Virtual Bandwidth on VAP with
yes
Decrease
END
Determine with
yes
yes
no
and
no
Increase
yes
no
Adjust
Notes: 2분

## Slide 21: Algorithm
Normal
Over AP’s timeslot
Request with
Provide streaming with
no
Initialize and
and
or
and
Calculate Virtual Bandwidth on VAP with
yes
Decrease
END
Determine with
yes
yes
no
and
no
Increase
yes
no
Adjust
Notes: 2분

## Slide 22: Algorithm
Congestion
Over AP’s timeslot
Request with
Provide streaming with
no
Initialize and
and
or
and
Calculate Virtual Bandwidth on VAP with
yes
Decrease
END
Determine with
yes
yes
no
and
no
Increase
yes
no
Adjust
Notes: 2분

## Slide 23: Algorithm
Adjustment
Adjustment
Over AP’s timeslot
Request with
Provide streaming with
no
Initialize and
and
or
and
Calculate Virtual Bandwidth on VAP with
yes
Decrease
Adjust
END
Determine with
yes
yes
no
and
no
Increase
yes
no
Notes: 2분
Inner loop
Out loop

## Slide 24: Algorithm
Three Timeslot cases
  and
  and
  and or and
Adjustment (Outer loop)
  Using Bi-section method
Adjustment (Inner loop)
  Adjust according to bandwidth ratio
Adjustment
Adjustment
Notes: 1분
사용자들이 사용하는 자원이 언더 유틸라이즈 혹은 오버 유틸라이즈 될때 람다 조절
Timeslot 설명하고
만일 𝑥_31=1일 경우 두 번째 비율 큰 것 선택

## Slide 25: Algorithm
Adjustment (Outer loop)
Notes: 만일 𝑥_31=1일 경우 두 번째 비율 큰 것 선택

## Slide 26: Algorithm
Adjustment (Inner loop)
Notes: 만일 𝑥_31=1일 경우 두 번째 비율 큰 것 선택

## Slide 27
Experimental Results
Experimental Environment

## Slide 28: Experimental Environment
Device
  SDN Controller
    Ubuntu 16.04
    ONOS 1.13.0
  Media Server
    Window 10
    Python3 webserver
  Access Point
    Ubuntu 16.04
    Raspberry PI3
    Hostapd
  DASH Clients
    Window 10
    Palcon Proxy
System parameter |  |  | 
 | 0.01439 |  | 0.00001
 | 0.02866 |  | 1.0 sec
 | 0.02828 |  | 9.0 sec
 | 0.005873 |  | 
System parameter |  |  | 
 | 0.01439 |  | 0.00001
 | 0.02866 |  | 1.0 sec
 | 0.02828 |  | 9.0 sec
 | 0.005873 |  | 
Access
Point
Media
Server
SDN
Controller
DASH
Clients

## Slide 29: Experimental Environment
MPD bitrate
  [ 200, 400, 600, 800, 1000, 1200, 1400, 1600, 1800, 2000, 2200, 2400, 2600, 2800, 3000 ] kbps
DASH segment duration
  2 sec
Request bitrate
  3000 kbps
Bandwidth
  Traffic control: “Wondershaper”
    Uplink: 100 Mbps
    Downlink: 4.5 Mbps
  Curve-fitting: kbps
Notes: Frozen이 발생하는 조건 찾으면서 traffic control과 timeslot 값 정함
사실상 uplink 조건은 별로 의미 없음

## Slide 30: Experimental Environment
Situation
  Three cases
Scenario 1
Scenario 2
Scenario 3
< single >
< multi >
Notes: Single의 경우 RSSI 값을 기준으로 연결된 상태
RSSI의 경우 physical 레이어에서 결정하기 때문에 AP의 로드 상태를 알 수 없고 고려할 수 없다.

## Slide 31
Experimental Results
Performance Comparison of Other Algorithms

## Slide 32: Performance Comparison with Other Algorithms
DASH.js
  Decide AP based on strong RSSI
  Decide bitrate based on download throughput
Non cooperative SDN enabled APs
  Decide AP based on strong RSSI
  Same algorithm when decide bitrates

## Slide 33: Performance Comparison with Other Algorithms
Same video
  UE1: Big Buck Bunny
  UE2: Big Buck Bunny
  UE3: Big Buck Bunny
  UE4: Big Buck Bunny
Notes: 현면이형 피드백:
여기 그림 넣기

## Slide 34: Performance Comparison with Other Algorithms
Scenario 1 (AP1: UE1/2/3/4, AP2: None)
  Bitrate
  PSNR
Case Device | Cooperative SDN enabled Aps | Non cooperative SDN enabled APs | DASH.js
UE 1 | 1617.82 | 837.62 | 656
UE 2 | 1631.37 | 825.74 | 894
UE 3 | 1611.88 | 829.70 | 896
UE 4 | 1613.86 | 851.49 | 942
Average / STD | 1618.77 / 8.78 | 836.14 / 11.36 | 847 / 129.25
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 43.43 | 40.39 | 36.80
UE 2 | 43.44 | 40.33 | 38.16
UE 3 | 43.40 | 40.35 | 37.67
UE 4 | 43.41 | 40.48 | 37.55
Average / STD | 43.42 / 0.02 | 40.39 / 0.07 | 37.55 / 0.56

## Slide 35: Performance Comparison with Other Algorithms
Buffer state ( : consumed, : received, y: Mbytes, x: time)
UE 1
UE 2
UE 3
UE 4
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
DASH.js
Non cooperative SDN enabled APs
Cooperative SDN enabled APs
Notes: 초반 구간은 확인 결과 버퍼를 다 못 채우는 경향

## Slide 36: Performance Comparison with Other Algorithms
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 43.37 | 41.52 | 41.23
UE 2 | 43.35 | 41.56 | 40.45
UE 3 | 43.43 | 45.85 | 45.85
UE 4 | 43.37 | 41.55 | 40.64
Average / STD | 43.38 / 0.03 | 42.62 / 2.15 | 42.04 / 2.56
Scenario 2 (AP1: UE1/2/4, AP2: UE3)
  Bitrate
  PSNR
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 1598.02 | 1063.37 | 1292
UE 2 | 1592.08 | 1075.25 | 1142
UE 3 | 1598.02 | 3000.00 | 3000
UE 4 | 1611.76 | 1071.29 | 1112
Average / STD | 1600.00 / 8.34 | 1552.48 / 965.03 | 1636.5 / 912.404
Notes: 시나리오 1과 달리

## Slide 37: Performance Comparison with Other Algorithms
Buffer state ( : consumed, : received, y: Mbytes, x: time)
UE 1
UE 2
UE 3
UE 4
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
DASH.js
Non cooperative SDN enabled APs
Cooperative SDN enabled APs
Notes: 초반 구간은 확인 결과 버퍼를 다 못 채우는 경향

## Slide 38: Performance Comparison with Other Algorithms
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 43.37 | 43.25 | 43.34
UE 2 | 43.37 | 43.33 | 41.89
UE 3 | 43.34 | 43.38 | 42.50
UE 4 | 43.36 | 43.37 | 42.20
Average / STD | 43.36 / 0.01 | 43.33 / 0.06 | 42.48 / 0.62
Scenario 3 (AP1: UE1/2, AP2: UE3/4)
  Bitrate
  PSNR
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 1598.02 | 1580.20 | 1852
UE 2 | 1598.02 | 1580.20 | 1378
UE 3 | 1590.10 | 1603.96 | 1630
UE 4 | 1590.10 | 1596.04 | 1474
Average / STD | 1594.06 / 4.57 | 1590.10 / 11.88 | 1583.5 / 206.94

## Slide 39: Performance Comparison with Other Algorithms
Buffer state ( : consumed, : received, y: Mbytes, x: time)
UE 1
UE 2
UE 3
UE 4
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
DASH.js
Non cooperative SDN enabled APs
Cooperative SDN enabled APs
Notes: 초반 구간은 확인 결과 버퍼를 다 못 채우는 경향

## Slide 40: Performance Comparison with Other Algorithms
Different video
  UE1: Big Buck Bunny
  UE2: Big Buck Bunny
  UE3: Sintel
  UE4: Elephant Dream

## Slide 41: Performance Comparison with Other Algorithms
Scenario 1 (AP1: UE1/2/3/4, AP2: None)
  Bitrate
  PSNR
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 1724.75 | 881.19 | 944
UE 2 | 1742.57 | 902.97 | 844
UE 3 | 1366.34 | 687.13 | 808
UE 4 | 1578.22 | 788.12 | 718
Average / STD | 1602.97 / 174.09 | 814.85 / 98.65 | 828.5 / 93.47
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 43.71 | 40.64 | 38.93
UE 2 | 43.74 | 40.74 | 38.28
UE 3 | 42.57 | 43.82 | 41.90
UE 4 | 43.24 | 37.63 | 34.97
Average / STD | 43.53 / 0.55 | 40.71 / 2.53 | 38.52 / 2.84

## Slide 42: Performance Comparison with Other Algorithms
Buffer state ( : consumed, : received, y: Mbytes, x: time)
UE 1
UE 2
UE 3
UE 4
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
DASH.js
Non cooperative SDN enabled APs
Cooperative SDN enabled APs
Notes: 초반 구간은 확인 결과 버퍼를 다 못 채우는 경향

## Slide 43: Performance Comparison with Other Algorithms
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 43.81 | 41.90 | 40.39
UE 2 | 43.82 | 41.93 | 40.93
UE 3 | 46.02 | 48.25 | 48.20
UE 4 | 40.73 | 38.77 | 38.85
Average / STD | 43.60 / 2.17 | 42.71 / 3.98 | 42.09 / 4.17
Scenario 2 (AP1: UE1/2/4, AP2: UE3)
  Bitrate
  PSNR
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 1770.30 | 1148.51 | 986
UE 2 | 1776.24 | 1156.44 | 1180
UE 3 | 1384.16 | 3000.00 | 2946
UE 4 | 1603.96 | 1039.60 | 1266
Average / STD | 1633.66 / 184.51 | 1586.14 / 944.08 | 1594.5 / 908.58

## Slide 44: Performance Comparison with Other Algorithms
Buffer state ( : consumed, : received, y: Mbytes, x: time)
UE 1
UE 2
UE 3
UE 4
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
DASH.js
Non cooperative SDN enabled APs
Cooperative SDN enabled APs
Notes: 초반 구간은 확인 결과 버퍼를 다 못 채우는 경향

## Slide 45: Performance Comparison with Other Algorithms
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 43.83 | 43.59 | 43.47
UE 2 | 43.83 | 43.84 | 43.30
UE 3 | 46.05 | 46.02 | 45.90
UE 4 | 40.73 | 40.52 | 39.07
Average / STD | 43.61 / 2.19 | 43.49 / 2.26 | 42.94 / 2.84
Scenario 3 (AP1: UE1/2, AP2: UE3/4)
  Bitrate
  PSNR
Case Device | Cooperative SDN enabled APs | Non cooperative SDN enabled APs | DASH.js
UE 1 | 1778.22 | 1679.21 | 1854
UE 2 | 1780.20 | 1782.18 | 1702
UE 3 | 1384.16 | 1382.18 | 1642
UE 4 | 1592.08 | 1520.79 | 1400
Average / STD | 1633.66 / 188.28 | 1591.09 / 175.94 | 1649.5 / 188.75

## Slide 46: Performance Comparison with Other Algorithms
Buffer state ( : consumed, : received, y: Mbytes, x: time)
UE 1
UE 2
UE 3
UE 4
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
DASH.js
Non cooperative SDN enabled APs
Cooperative SDN enabled APs
Notes: 초반 구간은 확인 결과 버퍼를 다 못 채우는 경향

## Slide 47
Conclusion

## Slide 48: Conclusion
We proposed HTTP adaptive video streaming service over cooperative SDN-enabled Wi-Fi networks
  Existing DASH has a resource monopoly problem, causing unfairness of the overall resource
  SDN & multi interface can manage resources in terms of overall view
  Power consumption can be increased because of multi interface
Proposed bitrate and delivery ratio allocation
  Increases video quality
  Prevent buffer underflow

## Slide 49
Appendix

## Slide 50
Experimental Results
Performance Verification of Proposed System

## Slide 51: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 200 kbps | 200 kbps | 200 kbps | 200 kbps
PSNR | 31.27 db | 31.27 db | 31.27 db | 31.27 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 200 kbps | 200 kbps | 200 kbps | 200 kbps
PSNR | 31.27 db | 31.27 db | 31.27 db | 31.27 db
 | AP 1 | AP 2
Timeslot | 0.25 sec | 0.00 sec

## Slide 52: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 200 kbps | 200 kbps | 200 kbps | 200 kbps
PSNR | 31.27 db | 31.27 db | 31.27 db | 31.27 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 200 kbps | 200 kbps | 200 kbps | 200 kbps
PSNR | 31.27 db | 31.27 db | 31.27 db | 31.27 db
 | AP 1 | AP 2
Timeslot | 0.25 sec | 0.00 sec

## Slide 53: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 400 kbps | 400 kbps | 400 kbps | 400 kbps
PSNR | 35.14 db | 35.14 db | 35.14 db | 35.14 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 400 kbps | 400 kbps | 400 kbps | 400 kbps
PSNR | 35.14 db | 35.14 db | 35.14 db | 35.14 db
 | AP 1 | AP 2
Timeslot | 0.50 sec | 0.00 sec

## Slide 54: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 800 kbps | 800 kbps | 800 kbps | 800 kbps
PSNR | 39.00 db | 39.00 db | 39.00 db | 39.00 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 800 kbps | 800 kbps | 800 kbps | 800 kbps
PSNR | 39.00 db | 39.00 db | 39.00 db | 39.00 db
 | AP 1 | AP 2
Timeslot | 1.01 sec | 0.00 sec

## Slide 55: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 800 kbps | 800 kbps | 800 kbps | 800 kbps
PSNR | 39.00 db | 39.00 db | 39.00 db | 39.00 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 800 kbps | 800 kbps | 800 kbps | 800 kbps
PSNR | 39.00 db | 39.00 db | 39.00 db | 39.00 db
 | AP 1 | AP 2
Timeslot | 0.99 sec | 0.01 sec

## Slide 56: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1400 kbps | 1400 kbps | 1400 kbps | 1400 kbps
PSNR | 42.12 db | 42.12 db | 42.12 db | 42.12 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1400 kbps | 1400 kbps | 1400 kbps | 1400 kbps
PSNR | 42.12 db | 42.12 db | 42.12 db | 42.12 db
 | AP 1 | AP 2
Timeslot | 1.75 sec | 0.01 sec

## Slide 57: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1400 kbps | 1400 kbps | 1400 kbps | 1400 kbps
PSNR | 42.12 db | 42.12 db | 42.12 db | 42.12 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1400 kbps | 1400 kbps | 1400 kbps | 1400 kbps
PSNR | 42.12 db | 42.12 db | 42.12 db | 42.12 db
 | AP 1 | AP 2
Timeslot | 0.99 sec | 0.79 sec

## Slide 58: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 2800 kbps | 2800 kbps | 2800 kbps | 2800 kbps
PSNR | 45.99 db | 45.99 db | 45.99 db | 45.99 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 2800 kbps | 2800 kbps | 2800 kbps | 2800 kbps
PSNR | 45.99 db | 45.99 db | 45.99 db | 45.99 db
 | AP 1 | AP 2
Timeslot | 2.00 sec | 1.59 sec

## Slide 59: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 2000 kbps | 2000 kbps | 2000 kbps | 2000 kbps
PSNR | 44.11 db | 44.11 db | 44.11 db | 44.11 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 2000 kbps | 2000 kbps | 2000 kbps | 2000 kbps
PSNR | 44.11 db | 44.11 db | 44.11 db | 44.11 db
 | AP 1 | AP 2
Timeslot | 1.43 sec | 1.13 sec

## Slide 60: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1600 kbps | 1600 kbps | 1600 kbps | 1600 kbps
PSNR | 42.87 db | 42.87 db | 42.87 db | 42.87 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1600 kbps | 1600 kbps | 1600 kbps | 1600 kbps
PSNR | 42.87 db | 42.87 db | 42.87 db | 42.87 db
 | AP 1 | AP 2
Timeslot | 1.14 sec | 0.91 sec

## Slide 61: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1600 kbps | 1600 kbps | 1600 kbps | 1600 kbps
PSNR | 42.87 db | 42.87 db | 42.87 db | 42.87 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1600 kbps | 1600 kbps | 1600 kbps | 1600 kbps
PSNR | 42.87 db | 42.87 db | 42.87 db | 42.87 db
 | AP 1 | AP 2
Timeslot | 1.14 sec | 0.91 sec

## Slide 62: Performance Verification of Proposed System
4UE, 2AP, Big Buck Bunny
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 | -59 dBm | -54 dBm | -51 dBm | -52 dBm
AP 2 | -72 dBm | -60 dBm | -63 dBm | -72 dBm
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1400 kbps | 1400 kbps | 1400 kbps | 1400 kbps
PSNR | 42.12 db | 42.12 db | 42.12 db | 42.12 db
UE AP | UE 1 | UE 2 | UE 3 | UE 4
AP 1 |  |  |  | 
AP 2 |  |  |  | 
Bitrate | 1400 kbps | 1400 kbps | 1400 kbps | 1400 kbps
PSNR | 42.12 db | 42.12 db | 42.12 db | 42.12 db
 | AP 1 | AP 2
Timeslot | 0.99 sec | 0.79 sec

## Slide 63: Appendix
MPD
HTTP Server
Segments
MPD
SDN Controller
Multipath Agent
SDN Application
OVS
Media Server
Segments
AP Agent
Traffic Info Transmitter
Hostapd
Open Flow
Traffic Info Transmitter
DASH Client
Traffic Info Collector
Streaming Optimizer
HTTP Server

## Slide 64: Appendix
Over AP’s timeslot
Request with
Provide streaming with
no
Initialize and
and
or
and
Calculate Virtual Bandwidth on VAP with
yes
Decrease
END
Determine with
yes
yes
no
and
no
Increase
yes
no
Adjust