## Slide 1: Wireless Networks Jae Jun Ha Media Computing and Networking Laboratory POSTECH 2018-09-01
Notes: 세미나 발표를 시작하겠습니다.

## Slide 2: Contents
MAC layer
  Some backgrounds on Wireless channel
    Wireless versus Wired
    Fading
    Model
  Modulation
    Analog modulation
    Digital modulation
    Adaptive modulation
    Multi-carrier modulation

## Slide 3: MAC
Medium Access Control
Determines who/when to transmit a packet through channel
Provides MAC-specific framing
  Fragmentation, splitting into slots
Provides error control mechanism
  How to detect the errors
  How to correct the errors (ex ARQ, FEC, etc.)
Performs management functions
  QoS
  Handover
  Power saving, etc.

## Slide 4: Distributed vs Centralized
Distributed and contention-based
  Random Access
  Robust to a single point failure
  Good for bursty traffic in light load
Centralized and controlled
  Controlled by BS
  More controllable
Could be more efficient, esp. with many users in heavy load

## Slide 5: Random Access MAC
When node has packets to send
  Transmit without a priori coordination among nodes
  Two or more transmitting nodes  collision
Random access MAC protocol specifies
  How to detect collisions
  How to recover from collisions
Examples
  Slotted ALOHA, ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 6: Pure (unslotted) ALOHA
Unslotted ALOHA: simpler, no synchronization
When frame first arrives
  Transmit immediately
Collision probability increase
  Frame sent at collides with other frames sent in [-1, +1]

## Slide 7: Slotted ALOHA
Assumptions
  All frames same size
  Time is divided into equal size slots, time to transmit 1 frame
  Nodes start to transmit frames only at beginning of slots
  Nodes are synchronized
  If 2 or more nodes transmit in slot, all nodes detect collision
Operation
  When node obtain fresh frame, it transmits in next slot
  No collision, node can send new frame in next slot
  If collision, node retransmits frame in each subsequent slot with prob. P until success

## Slide 8: Slotted ALOHA
Pros
  Single active node can continuously transmit at full rate of channel
  Highly decentralized: only slots in nodes need to be in sync
  simple
Cons
  Collisions, wasting slots
  Idle slots
  Nodes may be able to detect collision in less than time to transmit packet

## Slide 9: CSMA
Carrier Sense Multiple Access
Listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission

## Slide 10: CSMA/CD
Carrier Sense Multiple Access / Collision Detection
Carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing channel wastage
Collision detection
  Easy in wired LANs: measure signal strengths, compare transmitted, received signals
  Difficult in wireless LANs: receiver shut off while transmitting

## Slide 11: CSMA/CA
Carrier Sense Multiple Access / Collision Avoidance
Sender
  If sense channel idle for DISF sec., then transmit entire frame (no collision detection)
  If sense channel busy then binary backoff
Receiver
  If received OK return ACK after SIFS (ACK is needed due to hidden terminal problem)

## Slide 12: Hidden Terminal Problem
Notes: 숨겨진 노드 문제 (Hidden Terminal Problem)
무선 LAN에서 3개의 노드가 있을 때, 중간 1개 노드는 양 노드가 보여 통신이 가능하나, 2개 사이에는 통신이 불가 그래서 둘다 가운데 노드에게 신호를 보낼 때 서로 보낸 지를 모르기 때문에 충돌이 일어날 수 있음
http://www.ktword.co.kr/abbr_view.php?m_temp1=3262 + 첨언

## Slide 13: CSMA/CA
Problem
  Two nodes, hidden from each other, transmit complete frames to base station
  Wasted bandwidth for long duration!
Solution
  small reservation packets
  Nodes track reservation interval with internal “network allocation vector” (NAV)

## Slide 14: CSMA/CA
Sender transmits short RTS (Request To Send) packet
  indicates duration of transmission
Receiver replies with short CTS (Clear To Send) packet
  Notifying (possibly hidden) nodes
Hidden nodes will not transmit for specified duration: NAV

## Slide 15: Exposed Terminal Problem
Node B is transmitting to node A
Node C has a packet to be transmitted to node D
But, node C defers its transmission since node C is within node B’s transmission range
Node C is an exposed terminal to node B
  Reduction of channel utilization
Notes: Exposed Terminal Problem 이 먼지

## Slide 16: Centralized MAC: Static versus Dynamic
Static MAC well suited for circuit switching
  Voice-oriented 1G/2G cellular system
  Inefficient for packet switching, i.e. bandwidth is wasted when not utilized
Dynamic MAC is needed to handle various traffic patterns and QoS requirement
  Polling scheme
  Dynamic TDMA

## Slide 17: Dynamic TDMA
Frames divided into resource request (i.e. mini slots) and data slots
  ALOHA variations be used for request
  Data slots are allocated based on requests and scheduling

## Slide 18: Polling MAC
A master polls a slave for the transmission
  Based on the polling order scheduling
  TDD inherently
A master polls a slave for the transmission
Concern
  Polling overhead
    When the traffic load is light, polling overhead is relatively high
  Latency, especially when lightly loaded
  Single point of failure (master node)