## Slide 1: Wireless Networks Jae Jun Ha Media Computing and Networking Laboratory POSTECH 2018-08-24
Notes: 세미나 발표를 시작하겠습니다.

## Slide 2: Contents
PHY layer
  Background
  Modulation
    Analog modulation
    Digital modulation
    Adaptive modulation
    Multi-carrier modulation
Research
Notes: MAC 레이어는 다음 시간에

## Slide 3: Background
Limited radio resources
Less reliable communication channel
  Fading, shadowing, background noise
  Interference
Mobility
  Due to mobility, less reliable
  handover
Time-varying wireless environment
Broadcast nature of channel
  Multiple access mechanism is required to share the medium
  Less secure
Notes: Fading -> 시간에 따라 신호세기가 자주 변하는 현상
Shadowing -> 전파가 산이나 건물들에 막혀서 전달되지 않는 경우

## Slide 4: Background
Wireless != Mobile
  Wireless node may be static and fixed
  Mobile node may be using a wired networking
Infrastructure vs Ad hoc
  Infrastructure
    Access point (or base station) as an interface between wireless and (wired) backbone
  Ad hoc
    Wireless multi-hop transmission
    Peer-to-peer
https://learn.sparkfun.com/tutorials/connectivity-of-the-internet-of-things/infrastructure-and-ad-hoc-networks-
Notes: Wireless node의 예시 센서들, 고정 돼있으면서 무선으로 통신
Mobile node의 예시 노트북, 움직일 수 있다. 하지만 유선 네트워크를 사용할 수 있음

## Slide 5: Background
Wireless Channel
  It is a transmission medium for air waves.
  It has limitations on the performance
    Fading, shadowing
    Interference
Notes: 성능에 제약이 많아서 절대 원형 형태로 신호가 전파될 수 없다.

## Slide 6: Background
Statistical Fluctuations
  Local-mean power (large scale fading)
    Caused by local shadowing effects
    Slow variations
    Log-term variations
  Instantons power (small scale fading)
    Fast variations(over short time period and small distances)
    Caused by multipath reception, mobility, transmission bandwidth of signal
https://www.slideshare.net/vickydone/fading-and-large-scale-fading
Notes: Fading 말로 설명하고 넘기기(PT 양 너무 많이 나옴)
Local shadowing: 전파가 산이나 건물들에 막혀서 전달이 잘 안됨
Multi path: 멀티 패스 컴포넌트들이 임의의 위상과 진폭을 가짐
Mobility: 도플러 효과 물체와 움직이는 대상 사이의 속도 차로 인함
신호 채널 대역폭: 신호 및 채널의 대역폭 크기 차이에 따라, Flat fading과 Frequency Selective Fading유발
http://www.ktword.co.kr/abbr_view.php?m_temp1=3889

## Slide 7: Background(삭제 고민 중…, 만약 할꺼면 레일리 넣기)
Fast & Slow Fading
  Fast fading
    High Doppler spread
    Coherence time < Symbol period
  Slow fading
    Low Doppler spread
    Coherence time > Symbol period
Notes: Slow fading에 레일리히, 라이시안 분포 확률 해석(말로 설명)
http://www.ktword.co.kr/abbr_view.php?m_temp1=3889
상관 시간 심볼 시간이 먼지?

## Slide 8: Modulation
To transmit (analog/digital) message through wireless channel (even wired channel)
  To reduce noise and interference
  For channel assignment
  For multiplexing or transmission of several messages over a single channel
Analog Modulation
Digital Modulation
Notes: 아날로그 변조: 아날로그 데이터의 진폭에 따라 반송파의 진폭, 주파수, 위상을 변형시킴
디지털 변조: bit stream을 symbol의 나열로 나타냄

## Slide 9: Analog Modulation
Linear Modulation
  AM (Amplitude Modulation)
Angle Modulation
  PM (Phase Modulation)
  FM (Frequency Modulation)
Notes: Linear Modulation: 진폭의 변화를 통해 정보를 담음
Angle Modulation: 진폭은 일정, 위상이나 주파수의 변화를 통해 정보를 담음
FM에서 미분 식의 의미는 속도, 속도는 주파수에 비례해서 이런 식이 나왔다 설명

## Slide 10: Digital Modulation
Linear Modulation
  AM (Amplitude Modulation)
Angle Modulation
  PM (Phase Modulation)
  FM (Frequency Modulation)